FIRE FIGHTING ROBOT USING MICROCONTROLLER 8051

ABSTRACT

The project is designed to develop a fire fighting robot using RF technology for remote operation. The robotic vehicle is loaded with water tanker and a pump which is controlled over wireless communication to throw water. An 8051 series of microcontroller is used for the desired operation.

At the transmitting end using push buttons, commands are sent to the receiver to control the movement of the robot either to move forward, backward and left or right etc. At the receiving end three motors are interfaced to the microcontroller where two of them are used for the movement of the vehicle and the remaining one to position the arm of the robot. The RF transmitter acts as a RF remote control that has the advantage of adequate range (up to 200 meters) with proper antenna, while the receiver decodes before feeding it to another microcontroller to drive DC motors via motor driver IC for necessary work. A water tank along with water pump is mounted on the robot body and its operation is carried out from the microcontroller output through appropriate signal from the transmitting end. The whole operation is controlled by an 8051 series microcontroller. A motor driver IC is interfaced to the microcontroller through which the controller drives the motors.

Further the project can be enhanced by interfacing it with a wireless camera so that the person controlling it can view operation of the robot remotely on a screen.

BLOCK DIAGRAM TRANSMITTER

BLOCK DIAGRAM RECEIVER

# Text boxes

SOFTWARE REQUIREMENTS:

Kiel compiler,

Language:  Embedded C or Hex Assembly

HARDWARE REQUIREMENTS:

Micro controller unit (AT89C52),  Water pump, relay driver IC, Motor driver IC, Motors, Resistors, Capacitors, Diodes, Transformer, Regulator

HARDWARE REQUIREMENTS

8051 series Microcontroller, Push Buttons, RF Tx-Rx, Encoder, Decoder, DC Motors, Relay, Transistor, Robot Body with Water Tank,  Resistors, Capacitors, Diode, Battery.

SOFTWARE REQUIREMENTS:

Keil compiler

Languages: Embedded C or Assembly.

8051

microcontroller

ASM/C PROGRAM

8051 microcontroller

ENCODER

RF MODULE TRANSMITTER

CONTROL BUTTON

6V battery

RF MODULE TRANSMITTER

DECODER

ASM/C PROGRAM

12V battery

MOTOR DRIVER IC

MOTOR 2

MOTOR 1

RELAY

PUMP